## Slide 1: Robotics
Erwin M. Bakker| LIACS Media Lab

## Slide 2: Organization and Overview
Period: February 15th - May 10th 2019
Time: Friday 09.00 – 10.45
Place: LIACS, Room 401 (Workshops Room 303)
Lecturer: Dr Erwin M. Bakker ( erwin@liacs.nl )
Assistant: Andrius Bernatavicius
NB E-mail your name and student number to erwin@liacs.nl
Schedule:
15-2 Introduction and Overview
22-2 Control Space, Locomotion and Kinematics
1-3 Inverse Kinematics and Sensors
8-3 Yetiborg Introduction and SLAM Workshop I
15-3 Project Proposals (presentation by students)
22-3 Yetiborg Qualification and ROS Workshop II
29-3 Robotics Image Processing
5-4 Yetiborg Race and/or Nao Workshop III
12-4 Robotics Image Processing and Understanding
19-4 No Class
26-4 Robotics Reinforcement Learning.
3-5 Robotics Reinforcement Learning Workshop IV
10-5 Project Demos (by students)
Website: http://liacs.leidenuniv.nl/~bakkerem2/robotics/
Grading (6 ECTS): Presentations and Robotics Project (60% of grade). Class discussions, attendance, workshops and assignments (40% of grade). It is necessary to be at every class and to complete every workshop.

## Slide 3: Overview
Configuration Space
Rigid Body Motion
Forward Kinematics
Inverse Kinematics
Sensors
Link: http://modernrobotics.org
K.M. Lynch, F.C. Park, Modern Robotics: Mechanics, Planning and Control, Cambridge University Press, 2017

## Slide 4: How to move to a goal?
Problem: How to move to a goal?
Grasp, Walk, Stand, Dance, Follow, etc.
Solution:
Program step by step
  Computer Numerical Control (CNC), Automation.
Inverse kinematics:
  take end-points and move them to designated points.
Tracing movements
  by specialist, human, etc.
Learn the right movements
  Reinforcement Learning, give a reward when the movement resembles the designated movement.
Notes: C:\Users\admin\Desktop\OpenDag 2013\mydemos\bullet-2.75 ragdoll

## Slide 5: Configuration Space
Robot Question: Where am I?
Answer:
The robot’s configuration: a specification of the positions of all points of a robot.
Here we assume:
Robot links and bodies are rigid and of known shape => only a few variables needed to describe it’s configuration.
K.M. Lynch, F.C. Park, Modern Robotics: Mechanics, Planning and Control, Cambridge University Press, 2017

## Slide 6: Configuration Space
Degrees of Freedom of a Rigid Body: the smallest number of real-valued coordinates needed to represent its configuration
x

## Slide 7: Configuration Space
Assume we have a coin with 3 points A, B, C on it.
In the plane A,B,C have 6 degrees of freedom:
(xA,yA) , (xB,yB) , (xC,yC)
A coin is rigid => 3 extra constraints on distances: dAB, dAC, dBC
are fixed, wherever the location of the coin would be.
The coin and hence A can be placed everywhere => (xA,yA) free to choose.
B can only be placed under the constraint that its distance to A would be equal to dAB. =>
freedom to turn the coin around A with angle ϕAB => (xA, yA, ϕAB ) are free to choose.
C should be placed at distance dAC, dBC from A and B, respectively => only 1 possibility, hence no degree of freedom added.
Degrees of Freedom (DOF) of a Coin
= sum of freedoms of the points – number of independent constraints
= number of variables – number of independent equations = 6 – 3 = 3

## Slide 8: Configuration Space
[1] Definition 2.1.
The configuration of a robot is a complete specification of the position of every point of the robot.
The minimum number n of real-valued coordinates needed to represent the configuration is the number of degrees of freedom (dof) of the robot.
The n-dimensional space containing all possible configurations of the robot is called the Configuration Space (C-space).
The configuration of a robot is represented by a point in its C-space.
Closed-chain robot: Stewart-Gough platform. [1]
Open-chain robot: Manipulator (in V-REP). [1]

## Slide 9: Degrees of Freedom of a Robot
A rigid body in 3D Space has 6 DOF
A joint can be seen to put constraints on the rigid bodies it connects
It also allows freedom to move relative to the body it is attached to.

## Slide 10: Degrees of Freedom of a Robot
A rigid body in 3D Space has 6 DOF
A joint can be seen to put constraints on the rigid bodies it connects
It also allows freedom to move relative to the body it is attached to.

## Slide 11: Degrees of Freedom of a Robot
Proposition (Grübler's formula)
Consider a mechanism consisting of
N links, where ground is also regarded as a link.
J number of joints,
m number of degrees of freedom of a rigid body (m = 3 for planar mechanisms and m = 6 for spatial mechanisms),
fi the number of freedoms provided by joint i, and
ci the number of constraints provided by joint i, where fi + ci = m for all i.
Then Grübler's formula for the number of degrees of freedom of the robot is
This formula holds only if all joint constraints are independent. If they are not independent then the formula provides a lower bound on the number of degrees of freedom.
N = 5 links
J = 4 joints
fi = 1, for all i
ci=2, for all i
Planar Mechanism DOF = 4

## Slide 12
Links: 1 + 3 + 3 + 6 + 3 + 1 = 17
Joints: 21: 9x R(1 dof) and 12 x S(3 dof)
m= 6

## Slide 13: Assignments
3x SRS
M=6, N = 1 + 3 x 3 = 10, J = 3 x 3, dof per leg 3 + 1 + 3
=> dof = 6 (10 – 1 – 9) + 3 x 7 = 21

## Slide 14: Topologies
Note: S1 x S1 = T2 (not S2)
Coordinates
Explicit Coordinates
Euclidean (x,y)
Polar (r,ϕ)
Combined (x,y) x (r, ϕ)
Implicit Coordinates
{ (x,y,z) | x2+y2+z2=1 }

## Slide 15: C-Space (Configuration Space)
How to describe a rigid body’s position and orientation in C-Space?
Fixed reference frame {s}
Reference fame attached to body {b}
Described by 4x4 matrix with 10 constraints (unit-length, orthogonal)
Matrix can be used to:
Translate or rotate a vector or a frame
Change the representation of a vector or a frame
  for example from relative to {s} to relative to {b}

## Slide 16: C-Spaces

## Slide 17: Task Space and Work Space
The SCARA robot is an RRRP open chain that is
widely used for tabletop pick-and-place tasks.
The end-effector configuration is completely
described by (x, y, z, φ)
task space R3 x S1 and
workspace as the reachable points in (x, y, z), since all orientations φ can be achieved at all reachable points.
The workspace is a specification of the configurations that the end-effector of the robot can reach.

## Slide 18: Rigid Body Motion
Rigid-body position and orientation (x, y, z, ϕ, θ, ψ)
Can also be described by 4x4 matrix with 10 constraints.
In general 4x4 matrices can be used for
  Location
  Translation + rotation of a vector or frame
  Transformation of coordinates between frames
Velocity of a rigid body: (∂x/∂t, ∂y/∂t, ∂z/∂t, ∂ϕ/∂t, ∂θ/∂t, ∂ψ/∂t)
Exponential coordinates:
Every rigid-body configuration can be achieved by:
Starting in the fixed home frame and integrating a constant twist for a specified time.
Direction of a screw axis and scalar to indicate how far the screw axis must be followed

## Slide 19: Rigid Body Motions in the Plane
Body
Fixed reference frame

## Slide 20: Rigid Body Motions in the Plane
{b} relative to {s}
{c} relative to {b}
Previously:
{c} relative to {s}
Note and verify: R = PQ, and r = Pq+p

## Slide 21: Rigid Body Motions in the Plane
{c} described by (R,r)
Move rigid body such that {d} coincides with {d’}.
(P, p) can be used to
Represent a configuration of a rigid body in {s}
Change the reference frame for vector representation.
Displace a vector or a frame.
Note: SCREW MOTION
The above rotation followed by a translation can also be expressed as a rotation of the rigid-body about a fixed point s by an angle β
Then {c’} described by (R’,r’):

## Slide 22: Rigid Body Motions in the Plane
{c} described by (R,r)
Move rigid body such that {d} coincides with {d’}.
Note: SCREW MOTION
The above rotation followed by a translation can also be expressed as a rotation of the rigid-body about a fixed point s by an angle β
(β, sx, sy) , where (sx, sy) = (0, 2)
In the {s}-frame rotate 1 rad/sec with
speed (vx,vy) = (2, 0) is denoted as:
S = (ω, vx, vy) = (1, 2, 0)
Following the screw-axis for an angle
θ = π/2 gives the displacement we want:
Sθ = (π/2, π, 0)
These are called the exponential coordinates for the planar rigid-body displacement.
Then {c’} described by (R’,r’):
(vx,vy) = (2,0)
1 rad/sec
Note:
- distance = vt
- distance along quarter circle with radius 2 equals π.

## Slide 23: Forward Kinematics
The forward kinematics of 3R Planar Open Chain can be written as a product of four homogeneous transformation matrices: T04 = T01T12T23T34, where
Home position M:

## Slide 24: Forward Kinematics: Product of Exponentials
PoE parameters also known as
Euler-Rodrigues parameters.
There are many other representations:
for example Denavit-Hartenberg (1955) representation is very popular, but can be cumbersome
In velocity kinematics Jacobians are used.

## Slide 25: Inverse Kinematics
Which angles θ1, and θ1 will lead to location (x,y)?
, hence
,and similarly
γ= atan2(y,x)
Law of cosines gives:
Answer:
In general: IK-Solvers

## Slide 26: Real Time Physics Modelling
https://pybullet.org/wordpress/
pybullet KUKA
grasp training
Using Tensorflow
OpenAI gym
Baselines DeepQNetworks (DQNs)

## Slide 27: Robotics Preparations
1) Form YetiBorg Racing Teams of 3 to 4 people
Appoint one person who will be responsible for the robot.
Email your teams to erwin@liacs.nl with subject ‘Robotics YetiBorg Racing Team’.
Due: Thursday 7-3 at 14.00 PM.
2) Project Proposal Title and Abstract
Give the title and abstract of the project proposal you will present on March 15th.
Also mention the number of people that will cooperate on the project (1-4).
Email your proposal to erwin@liacs.nl with subject ‘Robotics Project Proposal’.
Due: Thursday 7-3 at 14.00 PM.
Notes: Laat plaatjes zien van oplossingen.

## Slide 28: References
K.M. Lynch, F.C. Park, Modern Robotics: Mechanics, Planning and Control, Cambridge University Press, 2017. ( DOI: 10.1017/9781316661239 )
https://pybullet.org/wordpress/

## Slide 29: Robotics